## Slide 1
LOW-DIMENSIONAL
MANIPULATION INTENT
An information budget for hierarchical dexterous control
How much information must a high-level intent carry to a dexterous controller?
Planners such as LLMs and VLMs can say what to do. We measure how compact the signal they pass to a 16-DoF controller can be.
Proposal · 3-minute pitch
PLANNER
LLM / VLM · slow
INTENT
k dimensions · f Hz
ACTION
RL policy · 16-DoF Allegro
Notes: [~10 s] Hi everyone. My project asks one question: how much information does a high-level intent need to carry to a dexterous robot hand?

## Slide 2
Problem: what should the intent interface carry?
01
High-level planner
LLM / VLM
what to do · updates in seconds
Manipulation intent ?
content · dimension · rate
the interface we study
Dexterous controller
RL policy, 16-DoF Allegro
how to do it · 30+ Hz contact control
RQ1
How many dimensions of intent does the controller need to reach expert performance, and should those dimensions describe the hand or the object?
RQ2
Does that budget grow when the task hides the goal and contact gets harder?
Task: in-hand cube reorientation in Isaac Lab. Everything except the intent signal stays fixed.
Notes: [~35 s] I split dexterous manipulation into three layers. At the top, a planner such as an LLM or VLM decides what to do, and it is slow. At the bottom, an RL controller moves sixteen finger joints at thirty hertz or more. The open question is what the middle layer should carry. So I ask two questions. First, how many dimensions of intent does the controller need, and should they describe the hand or the object? Second, does that budget grow when the goal is hidden and contact gets harder?

## Slide 3
Prior work picks one interface; none measures its budget
02
Hand-side intent
DexUMI (2025)
full hand pose via a wearable
TypeTele (2025)
manipulation types chosen by an LLM
CrossDex (2025)
eigengrasp action space across hands
Object-side intent
Human2Sim2Robot (2025)
object trajectory + one hand pose
LUCID (2026)
object flow + palm pose from human video
Minimal signal
InDex (2026)
a single grasp-progress scalar
Santello et al. (1998)
2 synergies explain >80% of grasp postures
Open question
Which content, and how many dimensions, does the interface need? No study varies both under one fixed controller.
Each system above fixes one representation and reports task success; the information budget itself is never swept.
Sources: DexUMI (Xu et al., 2025); TypeTele (Lin et al., 2025); CrossDex (ICLR 2025); Human2Sim2Robot (2025); LUCID (2026); InDex (2026); Santello, Flanders & Soechting (1998).
Notes: [~35 s] Recent systems each pick one interface. On the hand side, DexUMI transfers full hand pose, TypeTele lets an LLM choose among manipulation types, and CrossDex uses eigengrasps as a shared action space. On the object side, Human2Sim2Robot and LUCID pass object motion plus a palm pose. InDex goes to the extreme with a single progress scalar. But each system fixes one representation. Nobody has swept the content and the dimension of the interface under the same controller. That is the gap.

## Slide 4
Approach: oracle intent, compressed to k dimensions
03
Expert PPO
sees the goal
Oracle intent
at the student's state
Hand-k
PCA of expert finger action
Object-k
cube sub-goal or progress
Student PPO
intent + robot/cube state
Sweep k
0
1
2
4
8
16
k = 0: no intent (lower bound) k = 16: full hand
Why an oracle: intent is computed on the student’s own state, so no offline human sequence has to be aligned with simulation.
Where human hands enter: camera hand data builds a human synergy basis, tested against the robot’s own basis.
Notes: [~45 s] I first train an expert that sees the goal. At every step, I query it on the student’s own state and compress its output in two ways. Hand intent is the PCA projection of the expert’s finger action. Object intent is a cube sub-goal or a progress value. In the main setting the student cannot see the goal, so the intent is its only source of task information. I sweep k from zero to sixteen. This avoids aligning offline human recordings with simulation. Human hand data from a camera is used only to build a human synergy basis, which I compare against the robot’s own.

## Slide 5
Evaluation: how much performance each intent recovers
04
Primary metric
Recovery = (P − P_blind) / (P_oracle − P_blind)
0 = no better than no intent · 1 = as good as seeing the goal
Success rate
final consecutive successes
N₈₀
steps to 80% of expert
AUC
area under learning curve
3 seeds per condition · identical evaluation episodes
Expected output (illustrative)
0
1
2
4
8
16
intent dimension k
Recovery
hand
object
knee = needed budget
Notes: [~25 s] The main metric is recovery: how much of the gap between no intent and seeing the goal each condition closes. I also report success rate, steps to reach 80 percent of the expert, and learning-curve area, over three seeds. The deliverable is a curve like this one. Where it bends tells us how much information the interface actually needs, for hand intent versus object intent.

## Slide 6
Timeline: core results by Oct 25, report due week of Dec 1
05
Setup
Sep 29 – Oct 11
Stage 1 · core
Oct 12 – Oct 25
Stage 2
Oct 26 – Nov 15
Write report
Nov 16 – Nov 29
G0
G1
G2
Setup
Isaac Lab Allegro task, expert policy, robot synergy basis
Stage 1 · must finish
Goal visible; hand vs object intent at k = 0, 2, 4, 16
Stage 2
Goal hidden, full k-sweep; then either a second task or a human synergy basis
Future work
Slow-update sweep; an LLM picking sub-goals at ~1 Hz
Gates: each stage starts only if the previous one produced complete curves. No new experiments after Nov 15.
Expected contribution
1
An information-budget curve for the intent interface
2
Hand vs object intent at equal dimension
3
Groundwork for slow planners driving fast hands
Notes: [~30 s] The final report is due the week of December first, so I have about nine weeks. The first two set up the environment and the expert. Stage one, by October twenty-fifth, is the must-finish core: hand versus object intent at a few values of k. Stage two hides the goal and runs the full sweep, and the last two weeks are for writing. Slow intent updates and an LLM planner are future work. The result would be a measured information budget for the interface between a planner and a dexterous hand. Thank you.