## Slide 1
LOW-DIMENSIONAL
MANIPULATION INTENT
An information budget for hierarchical dexterous control
How much information must a high-level intent carry to a dexterous controller?
Planners such as LLMs and VLMs can say what to do. We measure how compact the signal they pass to a 16-DoF controller can be.
Proposal · 3-minute pitch
PLANNER
LLM / VLM · slow
INTENT
k dimensions · f Hz
ACTION
RL policy · 16-DoF Allegro
Notes: [~8 s] Hi everyone. My project asks how much information a high-level intent needs to carry to a dexterous robot hand.

## Slide 2
Problem: what should the intent interface carry?
01
High-level planner
LLM / VLM
what to do · updates in seconds
Manipulation intent ?
content · dimension · rate
the interface we study
Dexterous controller
RL policy, 16-DoF Allegro
how to do it · 30+ Hz contact control
RQ1
How many dimensions of intent does the controller need to reach expert performance, and should those dimensions describe the hand or the object?
RQ2
Does that budget grow when the task hides the goal and contact gets harder?
Task: in-hand cube reorientation in Isaac Lab. Everything except the intent signal stays fixed.
Notes: [~30 s] I split dexterous manipulation into three layers. A planner, such as an LLM, decides what to do, but it is slow. An RL controller moves sixteen finger joints at thirty hertz or more. The open question is what the middle layer should carry. So I ask: how many dimensions of intent does the controller need, and should they describe the hand or the object? And does that budget grow when the goal is hidden and contact gets harder?

## Slide 3
Prior work picks one interface; none measures its budget
02
Hand-side intent
DexUMI (2025)
full hand pose via a wearable
TypeTele (2025)
manipulation types chosen by an LLM
CrossDex (2025)
eigengrasp action space across hands
Object-side intent
Human2Sim2Robot (2025)
object trajectory + one hand pose
LUCID (2026)
object flow + palm pose from human video
Minimal signal
InDex (2026)
a single grasp-progress scalar
Santello et al. (1998)
2 synergies explain >80% of grasp postures
Open question
Which content, and how many dimensions, does the interface need? No study varies both under one fixed controller.
Each system above fixes one representation and reports task success; the information budget itself is never swept.
Sources: DexUMI (Xu et al., 2025); TypeTele (Lin et al., 2025); CrossDex (ICLR 2025); Human2Sim2Robot (2025); LUCID (2026); InDex (2026); Santello, Flanders & Soechting (1998).
Notes: [~25 s] Recent systems each pick one interface. DexUMI transfers full hand pose, TypeTele lets an LLM choose manipulation types, and CrossDex uses eigengrasps. Human2Sim2Robot and LUCID pass object motion instead, and InDex uses a single progress scalar. But each fixes one representation. Nobody has swept the content and dimension of the interface under the same controller. That is the gap.

## Slide 4
Approach: oracle intent, compressed to k dimensions
03
Expert PPO
sees the goal
Oracle intent
at the student's state
Hand-k
PCA of expert finger action
Object-k
cube sub-goal or progress
Student PPO
intent + robot/cube state
Sweep k
0
1
2
4
8
16
k = 0: no intent (lower bound) k = 16: full hand
Why an oracle: intent is computed on the student’s own state, so no offline human sequence has to be aligned with simulation.
Where human hands enter: camera hand data builds a human synergy basis, tested against the robot’s own basis.
Notes: [~30 s] I first train an expert that sees the goal. At every step, I query it on the student’s own state and compress its output in two ways: hand intent, the PCA projection of the expert’s finger action, and object intent, a cube sub-goal or progress value. I sweep k from zero to sixteen. This avoids aligning offline human recordings with simulation. Camera hand data is used only to build a human synergy basis for comparison.

## Slide 5
Setup: one task, one controller, only the intent changes
04
Testbed
Task
Isaac Lab Allegro cube reorientation
Robot
16-DoF Allegro hand, fixed palm
Learner
PPO, GPU-parallel environments
Fixed
reward, hyperparameters, training budget
Seeds
3 per condition
Stage 1 · goal visible
Does intent speed up learning?
Blind
Hand-2
Hand-4
Hand-16
Obj-1
Obj-4
6 conditions × 3 seeds = 18 runs
Stage 2 · goal hidden from the actor
The critic still sees the goal; intent is the only task signal.
Blind
Goal-oracle
Hand-1 … 16
Obj-1/3/4
Hand-3 + Obj-1
About 30 runs; then one extension: a second task or a human synergy basis
Notes: [~25 s] The testbed is Isaac Lab’s Allegro cube reorientation task, trained with PPO in parallel environments. Reward, hyperparameters and training budget are fixed; only the intent changes. Stage one keeps the goal visible and compares six conditions. Stage two hides the goal from the actor, keeps it for the critic, and runs the full sweep.

## Slide 6
Evaluation: how much performance each intent recovers
05
Primary metric
Recovery = (P − P_blind) / (P_oracle − P_blind)
0 = no better than no intent · 1 = as good as seeing the goal
Success rate
final consecutive successes
N₈₀
steps to 80% of expert
AUC
area under learning curve
3 seeds per condition · identical evaluation episodes
Expected output (illustrative)
0
1
2
4
8
16
intent dimension k
Recovery
hand
object
knee = needed budget
Notes: [~20 s] The main metric is recovery: how much of the gap between no intent and seeing the goal each condition closes. I also report success rate, steps to eighty percent of the expert, and learning-curve area, over three seeds. Where the curve bends tells us how much information the interface needs.

## Slide 7
Timeline: core results by Oct 25, report due week of Dec 1
06
Setup
Sep 29 – Oct 11
Stage 1 · core
Oct 12 – Oct 25
Stage 2
Oct 26 – Nov 15
Write report
Nov 16 – Nov 29
G0
G1
G2
Setup
Isaac Lab Allegro task, expert policy, robot synergy basis
Stage 1 · must finish
Goal visible; hand vs object intent at k = 0, 2, 4, 16
Stage 2
Goal hidden, full k-sweep; then either a second task or a human synergy basis
Future work
Slow-update sweep; an LLM picking sub-goals at ~1 Hz
Gates: each stage starts only if the previous one produced complete curves. No new experiments after Nov 15.
Expected contribution
1
An information-budget curve for the intent interface
2
Hand vs object intent at equal dimension
3
Groundwork for slow planners driving fast hands
Notes: [~22 s] The report is due the week of December first, so I have about nine weeks. Two weeks of setup, then stage one by October twenty-fifth as the must-finish core, then stage two until mid-November, and two weeks of writing. Slow intent updates and an LLM planner are future work. Thank you.