## Slide 1
LOW-DIMENSIONAL
MANIPULATION INTENT
for shared-autonomy dexterous control
How much human hand information is needed?
Task goal and object state can specify what to do. This proposal isolates how much human manipulation information is needed to make contact-rich execution learnable.
Proposal presentation
TASK
INTENT
ACTION
Notes: Opening framing: this is not a Quest teleoperation project. The scientific question is the information content of an intermediate manipulation representation between a task goal and 16-DoF control.

## Slide 2
The missing layer between task intent and dexterous action
02
Task-level intent
"rotate the cube"
Manipulation intent
?
Dexterous action
16-DoF Allegro
Language and VLMs
what to do
Contact-rich control
how to do it physically
RQ1
Does intermediate manipulation intent improve dexterous control beyond task and object state alone?
RQ2
Can low-dimensional hand synergies preserve the useful information in full hand tracking?
Controlled study: the representation changes; the task, policy and training setup stay fixed.
Notes: Problem definition. The task-level command and object state are assumed available. RQ1 tests whether human manipulation intent adds value. RQ2 asks whether a compact representation retains that value.

## Slide 3
Research gap: prior work changes the pipeline, not the information budget
03
Traditional teleoperation
Full human pose is retargeted to robot pose
Embodiment mismatch can distort contacts
DexUMI / DOGlove
Hardware improves feasible, precise demonstrations
Focus: collection quality and transfer
TypeTele / Dexplore
Types or soft references relax exact pose matching
Focus: better guidance under mismatch
UniDex
Unified action space and VLA scale across hands
Focus: generalization and data scale
Open question
How much intermediate human information is actually necessary?
Sources: TypeTele (Lin et al., 2025); DexUMI (Xu et al., 2025); Dexplore (Xu et al., 2025); DOGlove (Zhang et al., 2025); UniDex (Zhang et al., 2026).
Notes: Literature sources from the supplied folder: TypeTele: Releasing Dexterity in Teleoperation by Dexterous Manipulation Types; DexUMI: Using Human Hand as the Universal Manipulation Interface for Dexterous Manipulation; Dexplore: Scalable Neural Control for Dexterous Manipulation from Reference-Scoped Exploration; DOGlove: Dexterous Manipulation with a Low-Cost Open-Source Haptic Force Feedback Glove; UniDex: A Robot Foundation Suite for Universal Dexterous Hand Control from Egocentric Human Videos.

## Slide 4
Literature map along the representation abstraction axis
04
MORE HUMAN DETAIL
LESS HUMAN DETAIL
Full pose
DexUMI / DOGlove
Precise demonstrations
Fingertip geometry
Common retargeting signal
Contact-relevant structure
Synergy / type
TypeTele; latent skill codes
Compressed intent
Task goal only
VLA instruction + object state
No human motion
Our experiment
A controlled comparison across the same axis
The study tests whether performance saturates before full hand pose. A positive result would identify the smallest useful interface between high-level intent and dexterous control.
The axis organizes representation content, not hardware quality or overall system capability.
Notes: The abstraction axis is the synthesis of the supplied literature. TypeTele supports manipulation types as an abstraction. Dexplore supports soft reference guidance and compact latent skill conditioning. DexUMI and DOGlove represent rich human-state capture. UniDex motivates a language-conditioned, cross-hand control endpoint.

## Slide 5
Controlled comparison of four manipulation-intent representations
05
Task + object goal
Robot + object state
Object-only
0 human dims
Fingertips
medium dimension
PCA synergy
low dimension
Full hand
high dimension
Goal-conditioned PPO
16-DoF Allegro
Cube reorientation
Fixed across conditions
robot state • object state • reward • PPO • action space • training budget
Only the manipulation-intent representation changes.
Notes: Proposed system. Four conditions share the same task, state inputs, reward, PPO implementation, action space and budget. Object-only is the zero-human-information baseline. The other three increase or compress tracked hand information.

## Slide 6
Palm-normalized hand synergies isolate compact intent
06
Quest hand tracking
pᵢ in world frame
Palm-frame normalization
p̃ᵢ = Rₚₐₗₘ⁻¹(pᵢ − pₚₐₗₘ)
PCA encoding
zₜ = Wₖᵀ(hₜ − μ)
k = 4
Information supplied to the policy
Full hand
high
Fingertips
medium
PCA synergy
low
Object-only
zero
Wrist tracking defines the coordinate frame; the fixed-palm Allegro task does not treat wrist motion as a control variable.
Primary synergy setting: k = 4. A PCA-dimension ablation can test the compression-performance trade-off.
Notes: Representation design. Hand points are transformed from world coordinates into a palm-centered coordinate frame. PCA is fitted on normalized hand vectors. The main low-dimensional condition uses k=4; the exact hand vector h_t should be fixed before data collection and reported in the method section.

## Slide 7
Evaluation separates final performance from learning speed
07
Success rate
SR
Final task completion across held-out episodes
Sample efficiency
N₈₀
Steps required to reach 80% success
Learning-curve AUC
AUC = ∫ SR(n) dn
Performance accumulated over the full training budget
Experiment scale
1 seed
debugging
3 seeds
pilot
5 seeds
final
Secondary checks
final orientation error / robustness to tracking noise / representation dimension
Report mean and uncertainty across seeds; use identical evaluation episodes for all conditions.
Notes: Primary metrics: success rate, N80 and learning-curve AUC. Secondary analyses test final orientation error, tracking-noise robustness and representation dimension. One seed is only for debugging, three for a pilot, and five for the final comparison.

## Slide 8
Twelve-week execution plan and expected contribution
08
1–3
Build baseline
RL/PPO, Isaac Lab, Allegro task, object-only
4–6
Add intent
Quest preprocessing, fingertips, PCA synergy
7–10
Run study
Freeze setup, full-hand baseline, multi-seed runs, ablation
11–12
Validate and report
Real-data replay or demo, analysis, presentation
Expected contribution
1
Controlled evidence on the value of intermediate manipulation intent
2
A compression test for low-dimensional hand synergies
3
A candidate interface between task-level language and high-dimensional control
Primary cluster window: weeks 7–10. Local GPU work covers setup, debugging and single-seed pilots.
Notes: Timeline assumes the existing fixed-palm cube reorientation task. The strongest contribution is not VR control hardware. It is a controlled study of the interface: task intent to compact manipulation intent to dexterous control.